Memory & Caches
How it works, and how it affects performance
Matt Godbolt
@mattgodbolt

---
Outline
- Types of memory and their characteristics
  - Warning: some hairy hardware details
- Caches and how they work
- Measuring performance
- Virtual memory
- Multiprocessing

---
Types of RAM
- Static RAM
- Dynamic RAM
  - SDRAM
  - Rambus
- Non-volatile
  - ROM/PROM/EPROM/EEPROM
  - Flash RAM

---
1 Bit of Static RAM

---
Static RAM
- 6 transistors per bit
- Requires constant power VDD
- Logic-level inputs and outputs
- Regular repeating layout good for chip layout
- <1ns access times
- So why not make all RAM this way?
COST!

---
1 Bit of Dynamic RAM
AL
DL
C

---
Dynamic RAM
- One transistor per bit
- Leaks charge
  - Requires regular refresh
- Output is analogue
  - Requires external logic to tell 0 from 1
  - Needs time to charge/discharge
- Used in external chips
  - Need to minimise pin count (DDR3 240pins)

---
Dynamic RAM

---
Reading DRAM (short version)
- Precharge bit-lines (tRP ~2 memory cycles)
- Select row (tRCD ~3)
- Sense & latch row data (~8192 bits)
  - Feedback starts recharging cells
- Select column (CL ~2)
  - Data finally available
- Need tRAS (~8) cycles before next precharge

---
DRAM timings

---
Memory Controller
- Used to be in North Bridge
  - Now in CPU
  - Implications for SMP
- Opens/closes rows
- Reorders load/store
- Schedules refreshes
  - Every 64ms
- Handles DMA

---
Getting DRAM data out
- Memory bus runs at ~200MHz
- 64 bits transferred at a time
- Bits selected by column
- Bus 1x, 2x, 4x, 8x etc times per “clock”
  - DDR3 1600 = 200MHz bus x 8x pump x 64 bit
    = 12,800MB/sec
- Access times can dominate over data rates

---
Caching
- Static RAM is small and expensive
- Dynamic RAM is cheap, large, slow
- Use Static RAM as cache for slower DRAM
- But how to do this in hardware?
- Break into “entries” that can be cached

---
Finding a cache entry
- Organise data in “lines” of 64 bytes
  - Bottom 6 bits of address index into this
- Use some bits to choose a “set”
  - 5 bits for L1, 11 bits for L2, ~13 bits for L3

---
Finding a cache entry
- Search for cache line within set
  - L1: 8-way, L2: 8-way, L3: 12-way
- Remaining bits (“Tag”) used to find within set
- Why this way?

---
Caching

---
Timings and sizes
- Approximate timings for Sandy Bridge
- L1 32KB ~3 cycles
- L2 256KB ~ 8 cycles
- L3 10-20MB ~ 35 cycles
- Main memory ~ 250 cycles
  - Depends on all the things we spoke
    of earlier

---
Real-world measurements
- Measured on Westmere X5690
  - 32KB / 256KB / 12MB
  - Hope for similar timings to SB
- Time cost per access of pointer chasing
- Vary size of element and total working size

---
Results: Sequential Reads

---
Results: Sequential Reads

---
Discussion
- Automatic prefetching
  - Processor looks for patterns of cache misses coming from same instruction
- 8192 byte stride – what's going on there?
  - L3 cache is 12-way 12288-set associative
  - 1024, 2048, 4096 all divide into # of sets
  - 8192 does not divide into 12288

---
Sequential vs Random Reads

---
Random access measurements
- Why worse than worst-case RAM times?
  - Prefetching can hurt us
- Linear scan over data >5x better even for “small” data sets
- Program can prefetch
  - Hard to get right
  - Overrides Critical Word Load

---
Writes vs Reads

---
Write

---
Virtual Memory
- How do virtual addresses fit into this?
- Page tables require 4 reads to walk
Level 3 Index
Level 2 Index
      Offset
Level 4 Index
Level 1 Index
Page
L1 Directory
L2 Directory
L3 Directory
L4 Directory

---
TLBs
- Cache for translation, two-level 4-way
  - L1: 64 4KB page entries; 32 2MB page entries
  - L2: 512 4KB page entries
- Flushed on context switch
  - Although entries contain 12-bit “process” ID
  - Not needed for transition in/out of kernel

---
Virtual Memory and Caching
- L1 fast & small
  - Physically tagged, virtually indexed
  - 64 sets: bits 11:6 of address
  - DTLB read in parallel with cache fetch
- L2 and above larger and not so fast
  - Caches physical address

---
Example with Huge Pages

---
More on Huge Pages
← ~15cycles

---
Multiprocessing
- Bus between CPUs too slow to share all caches
- TLBs, L1 and L2 shared by hyperthreads on same core
- L3 shared by all cores on a socket
- How to achieve consistent view across all CPUs in a system?

---
MESI
- Modified
  - Exclusive, dirty
- Exclusive
  - Exclusive, non-dirty
- Shared
  - Possibly shared, non-dirty
- Invalid

---
MESI transitions
Somewhat expensive
Almost free
Pretty expensive

---
MESI
- Try to avoid Request For Ownership (RFOs)
- Minimum transaction is an entire cache line
- Pad data structures to a 64 bytes as needed

---
NUMA
- Most high end machines are NUMA
- Each socket has its own local RAM
- Accessing RAM on other sockets is slower
- Critical processes should allocate their own RAM

---
What can we do?
- Make good use of the cache
  - Keep data small
  - Try and scan linearly
  - Avoid pointer chasing
- Prefetch
  - Tricky to get right
- Bypass cache when appropriate
  - Non cache-polluting stores

---
Last slide
Questions?
Email: matt@godbolt.org
Twitter: @mattgodbolt
Based heavily on:
“What every programmer should know about Memory”
by Ulrich Drepper
http://www.akkadia.org/drepper/cpumemory.pdf